## Slide 1
Boeing Look at a Higher Speed 802.11 PHY
Delivered to the IEEE 802.11
Committee at Vancouver, BC, Nov 96
Notes: 1

## Slide 2
Agenda
Boeing Wireless Models
Evolution of Mobile Computing Comm
ISO Model
Limitations of 802.11 at Higher Speeds
Examination of the MAC Capabilities
Other Limitations
Proposal
Notes: 2

## Slide 3
Boeing Mobility Model
Boeing Campus
R
Regional Low
Speed Wireless
Campus High
Speed Wireless LANs
Notes: 3

## Slide 4
Boeing Campus
R
Boeing
Telephone
Switch
ATM
Factory Worker
Facilities Engineer
Collaboration
Campus Field Service
Boeing On-Campus Mobility Model
Warehouse & Inventory Control
Conference
Room
Information
Worker
Notes: 4

## Slide 5
Wireless
Wired
WAN Satellite
MANs/CANs
Cellular LAN
Personal Area
Networks
Wireless ATM
Home & Traveling
1996
1997
1998
1999
2000
2001
What is Going to Happen in Mobile Computing?
DBS
Worldwide Voice
analog(AMPS)
CDPD 19.2Kbps
PCS
2Mbps
IEEE 802.11
10-25Mbps
200Kbps
4Mbps
10Mbps
10-25Mbps
ISDN(128K)
Cable (10M)
Copper (6M)
Introduction
Limited Use
Large Scale
SMR
Dialed
4/24/96 RHP
Notes: 5

## Slide 6
Other Standards Activities
Wireless LAN Interoperability Forum (WLI)
Wireless ATM
Notes: 6

## Slide 7
ISO Model
MAC_SAP
PHY_SAP
MAC Sublayer
PLCP Sublayer
PMD_SAP
PMD Sublayer
MAC
Layer
Mgt
Entity
PLME_SAP
MAC
PHY
L
A
Y
E
R
L
A
Y
E
R
PLME_SAP
MLME_SAP
Station
Management
Notes: 7

## Slide 8
Limits on 802.11 at Higher Speeds
Limit in the 96microsec preamble plus 32microsec header plus packet transmit state timing for the PHY_SAP
At 25Mbps, 102791 bytes could conceivably be passed through the PHY_SAP. The largest size packet allowed through the present SAP is 4095 bytes.
MAC
PHY
L
A
Y
E
R
L
A
Y
E
R
96us
96X10-6s preamble+
32X10-6s header+
max 32760X10-6sX
25X106bps = 822328b
102791 octets
25Mbps
10Mbps
96X10-6s preamble+
32X10-6s header+
max 32760X10-6sX
10X106bps = 328880b
41110 octets
PHY_SAP
Notes: 8

## Slide 9
Limits on 2.4GHz at 10Mbps
1. 80Mhz-wide band
79 hops at 2Mbps (1MHz/channel), 16 hops at 10Mbps (5MHz/channel)
2. Channel Diversity
Decreasing number of channels increases interference
3. FCC Power Flux Density
Can’t cross the FCC power flux density requirements
4. Preamble Clock discovery
Above 2Mbps there could be clock jitter problems
Notes: 9

## Slide 10
Limits on NII/Supernet at 25Mbps
1. 350Mhz-wide band (5150-5350MHz and 5.725-5875MHz)
70 hops at 25Mbps (5MHz channels)
2. Channel Diversity
Still greater chance of interference at 70 vs 79 hops @ 1Mbps and 2Mbps
3. FCC Power Flux Density
From the NII/Supernet
4. Preamble Clock discovery
Much higher clocking speed
Notes: 10

## Slide 11
Results of the Future Work Meeting 11/11/96
Agenda:
Overview of user needs
Overview of other standards activities
Discussion
Modulation methods
Frequency allocations
How the new PAR meets the 5 criteria for PAR processing
Set requirements for the higher speed
Notes: 11

## Slide 12
Overview of User Needs
Boeing Presentation
ITT GLOMO Discussion
Lots of questions about Boeing requirements for wireless high bandwidth
Questions about the vendor position for customers such as Boeing-how
many customers are there like Boeing. Shouldn’t they be targeting
consumer or small company customers rather than the Boeings.
Lots of questions about the Boeing intent on three dimensional CAD.
The answer was that three dimensional CAD will be everywhere,
including in the warehouses and factories.
ITT attended the session with interest in delivery of information to
military people using high bandwidth wireless LAN technology.
Notes: 12

## Slide 13
Other Standards Activities
Vic Hayes gave a report on ETSI and Hiperlan
Hiperlan 1,2,3,&4
Hiperlan 1 is 5.1GHz
Hiperlan 2 is 17GHz
Hiperlan 3 is 60GHz
ece.wpi.edu for Hiperlan information
Vic mentioned that ETSI did not go to the ITU and so the
ITU is upset with ETSI and is refusing to do
business with them since they have not worked with the ITU.
Notes: 13

## Slide 14
Requirements for Higher Speed
Requirements/Objectives
Interoperability - preferred but not required (with 802.11 specification)
frequency band - should we consider higher speeds in the 2.4GHZ band
Start with about 150MHZ band near the NII and Hiperlan bands
Data rate - 25Mbps, consider fallback
Sensitivity (Range) - study will be conducted on spectral efficiency vs
sensitivity vs range vs immunity etc.
Transmit power - regulatory
Overlapping networks capability
Power consumption
Multipath immunity - methods more immune to multipath, ie work will be
conducted on channel models and immunity to multipath
Interference immunity - (modulation, protocol)
Economics (complex/efficient vs low cost) - complex/efficient vs low cost
Power consumption - mechanisms for power conservation (sleep modes)
Notes: 14

## Slide 15
Frequency Allocations
Conclusion: not important to specify the band but a range,
such as 150MHZ near NII frequencies
Notes: 15

## Slide 16
PAR Requirements
There are five criteria for a PAR:
Broad market potential
Compatibility
Distinct Identity
Technical Feasibility
Economic Feasibility
Notes: 16

## Slide 17
Create a new 10Mbps based on the NII/Supernet proposal
AND
Create a new 24 or 25Mbps based on the NII/Supernet proposal
Proposal
Notes: 17