## Slide 1
IEEE 802.11 Wireless Access Method and Physical Specification
Title: Issues and Trade-offs in High Speed 2.4 GHz PHY
Date: September 8, 1997
Author: Dean Kawaguchi
Symbol Technologies, Inc.
2145 Hamilton Ave
San Jose, CA. 95125
Telephone: (408)369-2629
FAX: (408)369-2737
email: DeanK@psd.symbol.com

## Slide 2
Introduction
Isues, concerns, and trade offs for a HS PHY in the 2.4 GHz band from a different viewpoint
  Interoperability with both FH and DS
  Interference and need for multiple channels
  Multipath
  1 vs 10 Mbps preamble and PLCP header
  Low cost and need for architectural option
Our alternative proposal would more effectively address these issues+
  DS spreading format
  Modulation and channelization
  Hopping and interoperability with 1&2 Mbps FH PHY
  Interoperability with 1&2 Mbps DS PHY
  Rate switching, 1 vs 10 Mbps preamble and PLCP header
  Comparison to 1&2 Mbps FH PHY
  Low cost, many architectural options
Subsequent submissions will address performance simulation/measurements

## Slide 3
Interoperability with both FH and DS
The high speed study group has decided in previous motions that there will be only one high speed PHY at 2.4 GHz
  Given the relatively large number of installed users of 802.11 ready FH PHY systems, it would be advantageous to provide compatibility with FH PHY systems as well as DS PHY systems
Obviously, given the different bandwidths of DS signals versus the 1 MHz FH PHY signals, there will be limited interoperability
  However, it is more than feasible to design units that can accommodate wideband and narrowband signals with the right definition
  Provisions for hopping and non-hopping will greatly enhance the ability of both FH and DS PHY to be at least partly interoperable with the high speed PHY

## Slide 4
Interference and need for multiple channels
As a manufacturer of both DS and FH systems, we have found that interference has necessitated the use of frequency agility even in DS systems
  Especially as the band got more crowded as occurred at 900 MH
  This will also happen soon in the 2.4 GHz band
Having multiple channels to use should be a requirement for the high speed PHY
  Having a mechanism to hop over the channels will be a big advantage as has been shown in the FH systems fielded today
  Frequency selectivity can provide typically 60 to 70 dB of isolation between channels
Direct sequence processing gain will also make the demodulator more robust because of Hamming distance

## Slide 5
Multipath and Robustness vs Bandwidth
Multipath distortion at the wider bandwidths requires the most robust modulations to mitigate its effects
Binary modulations are more robust than quadrature modulations, but requires twice the bandwidth
  10 Mbps would require 10 Mcps with QPSK and 8 chips/symbol and bandwidth of 20 MHz null to null
  BPSK would use 20 Mcps with bandwidth of 40 MHz null to null
  MSK would be in between at about 30 MHz
  16 chips/symbol would require about 60% more bandwidth, i.e., 32, 64, and 48 MHz
Binary FSK is one of the most robust modulations as the receive capture effect approaches 0 dBc in theory
  Binary GFSK also provides narrow bandwidth, e.g., a 20 Mcps FSK would have a 10 dB bandwidth approximately 22 MHz
DS processing will improve multipath performance in all cases above

## Slide 6
1 vs 10 Mbps preamble and PLCP header
The option to have 1 Mbps preamble is desirable, but the high overhead makes it difficult to achieve high throughput efficiency except in large packet situations
The option to be able to operate with 10 Mbps preamble, i.e., about 10% of the 1 Mbps preamble, would be necessary to meet expectations on throughput increases
Coherent QPSK operation with separate chipping sequences on I and Qwould require a longer preamble than the current DS PHY single chipping sequence (same on I and Q) over BPSK/QPSK
FSK would not require a longer preamble nor would it preclude it

## Slide 7
Low cost and many architectural options
There are many applications that could use wireless LANs
  These applications will span a wide range of requirements except for the common requirement of the lowest cost possible
The high speed PHY should allow for optimizing architectures to provide the best price/performance possible
  Better than forcing all applications to take a one size fits all solution.
  This will increase the target market for the HS PHY beyond what would be feasible with the one size fits all approach

## Slide 8
High Speed PHY Proposal
A succinct summary of the proposed high speed DS PHY is as follows:
  DS spreading: 4 bits/symbol and 8 chips/symbol bi-orthogonal Walsh codes
  Modulation: Binary GFSK with deviation h=0.7; 1.5 dB preemphasis
  Data rates: 1.25 Msym/sec (5 Mbps) and 2.5 Msym/sec (10 Mbps)
  Chipping rates: 10 Mcps and 20 Mcps
  Bandwidths: 11 MHz and 22 MHz

## Slide 9
DS Spreading Format
The DS spreading formats used by Harris and Micrilor uses simple yet effective bi-orthogonal Walsh codes
The 8 chips per symbol used by Harris is more bandwidth efficient which is crucial to satisfy the interference fighting channelization mentioned earlier
The 4 bits/8 chips per symbol used at 1.25 (or 1.375) Msps and at 2.5 Msps would produce 5 and 10 Mbps at a chipping rate 10 and 20 Mcps

## Slide 10
Modulation and channelization
The proposed modulation format is binary GFSK at 10 and 20 Mcps with a deviation of 7 and 14 MHz peak to peak (h = 0.7)
  The 10 dB bandwidth is roughly 11 and 22 MHz
  The modulation uses a combination of preemphasis and filtering to balance interference and multipath performance with desired spectral bandwidths
The channelization plan consists of 8 channels at 10 MHz spacing with 10 Mcps, and 4 channels at 20 MHz spacing with 20 Mcps

## Slide 11
Hopping and interoperability with 1&2 Mbps FH PHY
The hopping can be synchronized to interoperate with the 1 and 2 Mbps FH PHY
There are ten 1 MHz channels in each 10 MHz wideband channel and twenty in each 20 MHz wideband channel
When a particular 1 MHz channel is hopped to, the wideband channel which covers that 1 MHz channel is also used

## Slide 12
Interoperability with 1&2 Mbps DS PHY
The bandwidths proposed would be compatible with the current 11 Mcps used in 1 and 2 Mbps DS PHY
The DS PHY already provides for frequency selection interface with the MAC, similar to that used by the FH PHY (sans hopping algorithm)
The proposed format can use existing DS chip sets and architecture with changes primarily in the baseband processing to have a DS/HS design

## Slide 13
Rate switching, 1 Mbps vs high speed preamble and PLCP header
It is possible to use the current FH 1 Mbps preamble and switch to high speed operation after the PLCP header
  The remaining spare bit in the PLCP header could be used to indicate a x5 multiplier of the rate field
  The same tradeoffs of 1 Mbps preamble for interoperability and CCA discussed in the DS proposals apply
  Similar features can be made for DS preamble
Because of the bandwidth differences, it is preferable to use high speed preamble not only for overhead efficiency but also for the ability of FH/HS units to perform proper CCA on the HS signal
  For FH/HS BSS’s that may be using different hop sequences and tuned to a different 1 MHz channel within the same wideband channel, a high speed preamble would be better for implementing CCA on both narrowband and wideband channels.

## Slide 14
Sensitivity vs 1&2 Mbps FH
The Eb/No required of an FSK signal with an h=0.7 is 7 dB less than the 1 Mbps FH PHY which uses an h=0.32.
With a data rate of 5 Mbps, the noise bandwidth is 7 dB greater and the resulting signal requires a signal equal to that of the 1 Mbps FH PHY signal.
  The increase in bandwidth due to the DS spreading would be more than made up for in the despreading process.
  Thus the range of the 5 Mbps mode would be equivalent to the 1 Mbps FH PHY on a signal sensitivity basis alone, but will be degraded by the increase in multipath distortion and interference susceptability.
10 Mbps would be degraded by an additional 3 dB and even wider bandwidths and thus susceptability to interference and multipath.

## Slide 15
Interference and multipath
As mentioned earlier, narrower bandwidths, availability of multiple channels, and mechanisms to automatically hop among channels are all useful means by which to combat interference and multipath.
The binary GFSK modulation would allow the narrower bandwidth in the 5 Mbps mode, and the 10 Mbps would have a maximum 22 MHz bandwidth with a robust binary non-coherent FSK modulation.

## Slide 16
Low cost, many architectural options
An FSK system has been the lowest cost due to the simplicity, inherent robustness, and use of nonlinear components.
There are many options and design optimizations which will allow manufacturers to optimize for various applications and price/performance tradeoffs.
Intellectual property - Walsh codes and binary GFSK on wireless is probably not patentable any more.

## Slide 17
Feature Comparison Table
Feature Harris Micrilor Symbol
Modulation MOK BPSK/ MOK BPSK MOK BGFSK
coh QPSK (MSK?)
Data rates 5.5/11 Mbps 5/10 Mbps 5/10 Mbps
Bandwidths 22 MHz 32/64 (24/48?) 11/22 MHz
MHz
Number of channels 3/3 2/1 (4/2?) 8/4
Interoperability with FH None None Partial
Interoperability with DS Yes None Partial
Short preamble capable ? Yes Yes
Max J/I
Multipath