## Slide 1
SELECTION OF 5-GHz MODULATION
John H. Cafarella
MICRILOR, Inc.

## Slide 2
High Data Rate
Low Frame Overhead
  Non-Coherent: No PLL Settling
  Avoid Equalizer Adaptation Time
Multipath Tolerance
Low EB/N0
Desired Modulation Attributes

## Slide 3
Data Modulation Selection

## Slide 4
Modulation Approaches
Bandwidth Efficient Modulation
  Bandwidth = 1/Symbol Rate
  Complex Amplitude Modulation
  Constellation Crowded
Power Efficient Modulation
  Bandwidth >> 1/Symbol Rate
  Waveforms Very Different (PM/FM)
  Constellation Points Spread Out

## Slide 5
Synthesis from Orthogonal Functions
Traditional Orthogonal Signaling
  Transmit 1 of M Waveforms
  Non-Coherent
  Log2 M Bits of Information
Transmit Arbitrary 2 of M Waveforms
  Log2 M(M-1)/2 Bits of Information
  6.9 Bits for M=16
  Interesting, but Awkward to Encode

## Slide 6
Synthesis from Orthogonal Functions (cont.)
Structured 2 of M Waveforms
  1 of M/2 from 2 SubGroups
  2x3=6 Bits for M=16 (Two SubGroups of 8)
General: Structured 2K of M Waveforms
  1 of M/2K from 2K SubGroups
  Natural Subdivision of Walsh Functions
  2KxLog2(M/2K) Bits
Add Another Bit/SubGroup for BiOrthogonal

## Slide 7
Summary of Properties

## Slide 8
Data Transmission 1 of 16 plus DPSK
shift reg.
5
4
DPSK Mod.
Walsh fn. gen.
PN Code gen.
Baseband Transmit Signal
Chip Clock

## Slide 9
Data Transmission 4 times 1 of 4 plus DPSK
shift reg.
12
8
DPSK Mod.
Walsh fn. gen.
PN Code gen.
Baseband Transmit Signal
DPSK Mod.
DPSK Mod.
DPSK Mod.
fc
fc
S

## Slide 10
Data Demodulation
Baseband Walsh Symbol Correlator
I Channel
Signal
Baseband Walsh Symbol Correlator
Q Channel
Signal
Magnitude
&
determine largest
Index of Largest
DPSK Decision
Complex Amplitude of Largest
Z-1
Previous Complex Amplitude
2
Reconstruct
12-bit Demodulated Symbol
from 4
Channels
1

## Slide 11
Modulation Summary
24 Mbps Data Rate
  12 bit/symbol @ 2 Msymbol/s
  Multipath-Resistant
6 Channels in NII Band
  48-MHz Null-Null (32 Mchip/s MSK)
10-Mbps Fall-Back Mode