## Slide 1
SUMMARY OF THE DOCUMENT U-NII BAND CHANNELIZATION AND THE WINFORUM SRDC
Prepared for the Joint ETSI/BRAN and IEEE 802.11 Meeting
September 8-12, 1997

## Slide 2
PURPOSE OF THE DOCUMENT
Summarize the Objectives and Scope of the WINForum Sharing Rules Development Committee (SRDC)
Present the SRDC Fixed Channelization Proposal for the U-NII Band
Review the Part 15 Restricted Band Rules Effect on Out-of-Band Emissions
Preliminary Guard Band Calculations
Summary of the WINForum U-NII reconsideration petition

## Slide 3
Objectives and Scope of the SRDC
Obtain U-NII Spectrum
Interact with Regulatory Bodies to Set Rules for Use of the Band
Develop Spectrum Sharing Rules for the Industry

## Slide 4
Fixed Channelization Proposal
The U-NII Band Should Support Signaling Rates of 20 to 25 Mb/s
Mixed Bandwidth Potential Problem
  Wide Range of Potential Application Signaling Rates Needed
  Minimum Channel Spacing Required Because of Wide Signaling Rate Range and Mixed Bandwidth Incompatibility
  Detailed Technical Discussion of Mixed Bandwidth Problem in Appendix A
SRDC Recommends Fixed Frequency Assignment

## Slide 5
Part 15 Restricted Band Rules
Average and Peak EIRP Specified by the Part 15 Rules
The Power Spectral Density is Derived From This
  Based on some current interpretations which are still being investigated
Band Edge PSD 15-16 dB More Severe Than HIPERLAN Requirements for the U-NII Middle Band
Significant Guard Bands Needed

## Slide 6
Preliminary Guard Band Calculations
Characteristics of Intermodulation Distortion on Widening Transmitted Spectrum
Measurements Given in Appendix B of the Paper
Preliminary Estimate
  Example Intraband Channel Isolation Specs (30 dB PSD Adjacent Channel)
  1 to 1.3 Channels Widths of Guard Band Needed to Satisfy Restricted band Rules
  Further Study Needed

## Slide 7
U-NII Reconsideration Petition
Rulemaking not finalized
SRDC working closely with NTIA to resolve issues
9 issues addressed in reconsideration petition
Most important issues:
  total power output
  definition of measurement of power spectral density
    If denied: total power permitted 6-10 dB lower than limits specify