## Slide 1
Source: Chairman IEEE P802.11Task Group A
Title: IEEE P802.11 Tga Overview
Agenda item: Joint ETSI-IEEE meeting
Decision
Discussion
Information
Document for:
Decision/action requested
For information
September 1997
doc. IEEE P802.11-97/93
ETSI EP BRAN #4
WG3 Temporary document 70
15 September 1997
page 1

## Slide 2
IEEE P802.11 - ETSI BRAN WG3 meeting - September 1997 - 802.11 and TGa Overview
Naftali Chayat, BreezeCom
Task Group A Chair

## Slide 3
Long Term Goals for 802.11/BRAN Collaboration
Common PHY, different MACs
  Try having a common PHY sublayer
    to improve coexistence
    economy of scale
  cross-fertilization
Allow 802.11 MAC devices in Europe

## Slide 4
Preliminary MAC/PHY Models
Common PMD
ETSI Convergence
IEEE Convergence
ETSI MAC
IEEE MAC
connection oriented service
mixed connectionless and time bounded services
PHY
Data Link

## Slide 5
802.11 Overview - Topology
Peer-to-peer (Ad-Hoc) networks supported
Infrastructure based networks supported
  Access Points connect to a backbone
  Cells may overlap for continuity of service or increased capacity
802.11 assumes connectionless services

## Slide 6
802.11 PHYs Today
2.4 GHz Radio and IR
At 2.4 GHz, both DS and FH Spread Spectrum systems, as per ISM band regulations
Rates of 1 Mbit/s and 2 Mbit/s supported
  Task Group examines higher speeds at 2.4 GHz band

## Slide 7
802.11 MAC principles
CSMA/CA + Ack
Optional RTS/CTS before Data/ACK sequence
CCA and Virtual Carrier Sense as a medium sharing mechanism
Distributed Coordination Function (DCF) and Point Coordination Function (PCF)
  Time bounded services are provided by PCF (Point coordination function)

## Slide 8
802.11 Medium Sharing
Both Physical and Virtual Carrier Sense are implemented.
Virtual Carrier Sense
  Each packet in a transaction advertises the time at which transaction will end
  A Station hearing either of the sides will not transmit until the advertised time passes

## Slide 9
Task Group A - 5 GHz PHY
Started work in September 1997
Intends to produce and approve a supplement to 802.11 standard by July 1999
Focuses on US U-NII and European bands in 5 GHz (which overlap)
speeds about 20 Mbit/s

## Slide 10
TGa - Schedule
Requirements & Criteria Nov97
Text for all modulation proposals by (skeleton by Nov97/ Full text by Jan98)
  Deadline for modulation proposals (Nov97)
Modulation method selection - March98
Text finalization - March98+May98
Preapproval in March98 to send WG LB
Releasing Draft for WG LB from May98

## Slide 11
Modulation method proposals
GMSK/OQAM
M-ary Orth. Keying (MOK)
BiOrthogonal waveform sets
OFDM
GFSK

## Slide 12
Data rates and types of traffic
primary data rate about 20 Mbit/s + fallback rate? + highspeed?
Asynchronous data packets + Time bounded services
Asynch packets may be 4095 bytes long
Control packets (RTS,CTS, ACK etc..) are typically 20 bytes long

## Slide 13
Criteria for Comparison
multipath robustness
  The project focuses on indoor environments, but needs to maintain robustness at longer multipath
Sensitivity
  Sensitivity is defined for a flat channel at packet loss rate derived from a 10-5 BER

## Slide 14
Criteria for Comparison (cont.)
Overhead
  preamble
  backoff slot size
Channel width
  Number of channels available
  Adjacent channel interference
Power consumption, complexity, sensitivity to implementation

## Slide 15
Questions to ETSI
Coexistence with other systems (in particular, how will different HIPERLANs coexist?)
Does ETSI consider PHYs with multiple rates?
Does ETSI consider both long and short preambles?
Does ETSI have a position on use of directional antennae? (Power vs. EIRP; multipath reduction)
Information on availability of extra 50 MHz in Europe.