## Slide 1
September 8, 1997
Carl Andren, Harris Semiconductor
Suggested 802.11 High Rate PHY Technique
Harris High Rate data modulation
demonstration
Notes: 1
This paper discusses an approach for extending the 802.11 standard to accommodate high rates of 10 Mbps or better. Harris Semiconductor has a technique that it offers to the 802.11 as suitable for inclusion into the standard. Harris has implemented this technique in an integrated circuit and has performed tests on the first silicon which are reported here. The first samples of this device will be available for distribution late this year.

## Slide 2
September 8, 1997
Carl Andren, Harris Semiconductor
Standard Definition Issues
10+ MBps Physical Layer standard
  Provide backwards compatibility to IEEE 802.11 at 1&2 MBps?
  Separate or integrated section for higher rates?
Limited bandwidth available in the ISM bands
  Maximize bits/Hz
  Desire at least 3 channels
Meet FCC requirements for ISM bands
  FCC is comfortable with any solution that derives >10 dB from spreading function and passes CW test
  Preliminary testing shows that the Harris technique will pass
Textbook technique available without patent issues.
Notes: 2
The factors we need to address in the choice of an extension to the standard are:
Bandwidth occupied. We could up the spread rate, but the existing scheme is already down to 3 or 4 channels in the ISM band. Fewer channels is not an attractive idea.
We have sought guidance from the FCC and have gotten the following: If you can pass the CW jamming test and can show that your waveform derives over 10 dB from the spreading function, they have no problem with your waveform. For the purposes of the test, SNR can be defined as your theoretical Es/N0.
It is highly desirable to tie the existing standard into the loop. We have studied the question and concluded that the new rates can be incorporated along with the existing rates at the expense of retaining the PLCP header as is. This saddles the high rate system with an overly long preamble, but it makes the systems interoperable. This is very good in that the user can add high rate nodes as needed and use the lower rates to fill coverage gaps in the high rate system. The interleaved rate system will be well behaved and defer the medium for the appropriate length of time as desired. The low rate preamble will reach further than the message, but the power density will be the same.
The technique being suggested can be found in textbooks such as: “Telecommunications Systems Engineering”, by Lindsey and Simon, Prentice Hill, publisher.

## Slide 3
September 8, 1997
Carl Andren, Harris Semiconductor
Harris High Rate 802.11 Features
Provides 10+ MBps wireless LAN data rates while maintaining interoperability with 1 & 2 MBps WLANs
Increases data rate by >5x with no increase in the transmit bandwidth requirement
Rate switching during packets is supported already
1, 2, 5.5, &11 MBps capability
Fits in a PCMCIA package, uses existing RF and IF
Notes: 3
The benefits of a good high rate waveform are an increased longevity in the marketplace and no obsolescence of the early entries. By making the units interoperable, they can be introduced seamlessly into the market.
The new methods shown are benign in that they do not increase the current occupied bandwidth. Up to 5.5 times higher data rates are achieved.
The mechanism for rate switching has already been incorporated and the new rates fit with the definitions already established.
The increase in complexity of the high rate system does not alter the size of the hardware, so it will fit into a PCMCIA package.
We consciously decided to minimize the chip risk by eliminating some nice features such as short, high rate preambles in order to construct a chip to test the basic modulation scheme in the real environment and have a useful product.

## Slide 4
September 8, 1997
Carl Andren, Harris Semiconductor
Suggested Technical Approach
Utilize MOK/PSK modulation techniques to realize 4 to 8 bits/symbol
Use existing preamble and header to insure interoperability.
Increase symbol rate to 1.375 MSps (8 chip symbols) and hold existing spread rate
Use existing 802.11 DS parts for the RF & IF circuits
Notes: 4
The high rate scheme chosen will not impact the design of the RF and IF parts currently employed. This means a small redesign effort and the ability to drop in a new baseband processor into the existing radios to get the higher rates.
One issue to be addressed in the modem design is the switch to a different symbol rate once into the PDU. Since the spread rate is unchanged, this should be no difficulty.
The new scheme requires an absolute phase reference. The PLCP preamble is BPSK and as such, will provide a 180 degree phase ambiguity. By using the last bit out of the modulator prior to the PDU as a phase reference, we can establish an absolute phase reference.

## Slide 5
September 8, 1997
Carl Andren, Harris Semiconductor
Additional Modifications to Standard
Use last bit of PLCP header as an absolute phase reference for high rate demodulation.
Notes: 5
The 802.11 standard can be easily modified to accommodate the new waveform. The basic modifications are to the sections covering the DSSS PHY layer. The only modifications are to the actual modulation and resulting performance parameters. The current sections on DSSS contain separate sections on 1 and 2 MBps and this can be extended to cover the new rates. Some overall changes to the spread function also need to be addressed.
The PLCP header only needs to have the new rates added to the `list of acceptable rates.
A note in the modulation section to have the phase reference defined has to be added.

## Slide 6
September 8, 1997
Carl Andren, Harris Semiconductor
Performance Predictions
MOK modulation is slightly more efficient than BPSK due to embedded coding properties. Theoretical performance is 7.8 dB Eb/N0 for 1.0e-5 BER.
With 8 bits per symbol, Es/N0 is 16.8 dB.
Should readily meet -80 dBm sensitivity but, we might want to spec it at -75dBm to provide margin
Will pass FCC CW jamming test with margin
  J/S suffers with higher Es/N0
  FCC allows SNR to be defined as Es/N0
Notes: 6
The performance of the new waveform for higher rates has been modeled and simulated. The theoretical performance of MOK is well known and covered in general texts. Typically, it is somewhat better than BPSK since it has coding properties built into the waveform and sends code symbols rather than bits. Since the modulation carries 11 times as many bits as the 1 MBps case, it requires about 9 dB more Es/N0 than BPSK.
One primary concern is passing the FCC requirements on processing gain. We have queried the FCC about this waveform and have gotten an approval providing the waveform passes the CW jamming test. We also got the interpretation that the SNR in the test can be considered Es/N0.
Our simulations and tests show that it will pass the test under these interpretations.

## Slide 7
September 8, 1997
Carl Andren, Harris Semiconductor
Effects of Long Preamble
The use of the interoperable preamble will reduce the average data rate.
Longer packets will be less impacted.
Overall network loading will impact the effective rates.
A high rate preamble would alleviate these effects, but would eliminate interoperability.
Notes: 7
Long preambles cause a loss in effective transmission rate, but this still allows a higher rate than available without the high rate. The use of RTS/CTS/ACK protocols with the long preambles also substantially impacts the net throughput.
A side benefit of the long preambles is that equalizer schemes can be implemented using the preamble for training. With short preambles, this would not be available.

## Slide 8
September 8, 1997
Carl Andren, Harris Semiconductor
Effective rate versus packet size
Notes: 8
It is desirable to use long packets to minimize the impact of the long preambles. Users concerned with maximizing throughput will also avoid the RTS/CTS/ACK protocol options.

## Slide 9
September 8, 1997
Carl Andren, Harris Semiconductor
Effective rate versus packet size for short preambles
Notes: 9
Short preambles will significantly improve throughput at the cost of a loss of interoperability.

## Slide 10
September 8, 1997
Carl Andren, Harris Semiconductor
Loading Effect Assumptions
RetryMax=6, all transmissions are either successful or abandoned after RetryMax retries.
Load is the probability that the medium will be busy when sensed.
CCA is perfect and all stations can hear every other station (no transmissions are clobbered by hidden node problem).
Notes: 10
This spreadsheet analysis was done by Bob O’Hara and modified by Carl Andren.

## Slide 11
September 8, 1997
Carl Andren, Harris Semiconductor
Effective rate versus loading
Notes: 11

## Slide 12
September 8, 1997
Carl Andren, Harris Semiconductor
11 Bit Barker Word
56
59
65
6A
03
0C
30
3f
3-ary modified Walsh Functions
22 MHz
11 MBps
QMBOK
5.5 Mbps
BMBOK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS Bpsk
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit encoded to
2 code words
11 chips
1 MSps
2 bits encoded to
4 code words
8 chips
1.375 MSps
4 bits encoded to
16 code words
8 bits encoded to
2x16 code words
8 chips
1.375 MSps
I
Q
I,Q
I
Q
I,Q
Modulation Scheme
Notes: 12
The Harris suggested high rate modulation is a form of M-ary Bi-Orthogonal keying. We propose that both Binary and Quadrature forms of this modulation be used to provide multiple rates for stressed links.

## Slide 13
September 8, 1997
Carl Andren, Harris Semiconductor
Pick One
of 8 Walsh
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
1
MOK Modulation Approach for 11 MBps
Notes: 13
This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 14
September 8, 1997
Carl Andren, Harris Semiconductor
MOK properties
This modulation is the most power efficient available
The spectrum is like 802.11 DSSS
Multipath performance is nominal for the SNR
Requires a cover sequence to avoid the Wal0 CW modulation (modified Walsh Functions)
Requires coherent processing
Moderate implementation complexity (~25% extra)
Notes: 14
MOK modulation has been shown to have slightly better Eb/N0 performance than BPSK due to embedded coding properties. This makes the waveform the most power efficient of the many candidates. This allows the modulation to tolerate more interference than other waveforms. Since there are more bits per symbol with this modulation, it naturally requires more Es/N0 than BPSK, but the increase is minimized.
The spectrum of this waveform is sinx/x, which is the same as the 802.11 waveform now, but without some of the little blips that the 11 bit sequence causes.
The multipath performance will depend on the Eb/N0 and phase distortion tolerance of the waveform. We have shown through simulation, that this signal will have an adequate performance in the indoor environment. It is obviously worse than the 1 MBps case which can tolerate an SNR of 0 dB.
The Walsh function set includes one member that is all 0s. This is undesirable, but easily fixed by covering the sequence with another sequence which will not destroy the orthogonality.
To use both I and Q channels independently requires that the system process the signal coherently with an absolute phase knowledge. This is not a large concern as the PLCP preamble and header can supply the necessary means to lock up a PLL in a given state. This and the parallel correlators for the demodulation moderately increase the complexity of the demodulator.

## Slide 15
September 8, 1997
Carl Andren, Harris Semiconductor
MUX
1:4
3
DATA
IN
I,Q OUT
1.375 MHz
11 MHz
1
Data Rate = 4 bits/symbol * 1.375 MSps = 5.5 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
MOK Modulation Approach for 5.5 MBps
Notes: 15
Operating the basic MOK receiver with only the I channel modulated gives half the base rate and makes for a more rugged system. In this mode, the Q channel is turned off and the I channel supplied to both the I and Q channel modulator ports.
The receiver demodulator can use a limiter since the desired signal dominates in the IF bandwidth. This makes it simpler to implement than an AGCd design.

## Slide 16
September 8, 1997
Carl Andren, Harris Semiconductor
5.5 MBps properties
The 5.5 MBps mode uses BPSK modulation which is much more rugged than QPSK
This modulation will achieve comparable range to the 2 MBps QPSK 802.11 mode.
Stations can easily fall back to this mode when stressed, then 1 MBps if really stressed.
Notes: 16
The BPSK MOK mode has twice the phase tolerance and is therefore more rugged with respect to phase disturbances due to channel distortion due multipath. It is also 3 dB more sensitive.
Since multipath is one of the greatest limitations to range and effects QPSK much more than BPSK, this mode is expected to operate almost as good as the QPSK 2 MBps mode.
In an 802.11 network, this provides a good intermediate fallback rate for stressed links. The network access point can negotiate for the best rate supportable with each station. Having rates of 1, 2, 5.5, and 11 MBps, allows a large variation to account for gap filling and other network necessities.

## Slide 17
September 8, 1997
Carl Andren, Harris Semiconductor
HFA 3860 BER performance
Notes: 17
The expected performance of the MBOK technique can be derived from various texts and shows an improvement over PSK of about 1.6 dB. The achieved performance for a low cost implementation has about 3 dB or less of implementation loss.

## Slide 18
September 8, 1997
Carl Andren, Harris Semiconductor
HFA 3860 PER performance
Notes: 18
The packet error rates generally follow the bit error rate curves adjusted for the number of bits. The deviations are due to acquisition performance. Generally, however the SNR of the 1 Mbps preamble and header is so high that the acquisition is usually perfect.

## Slide 19
September 8, 1997
Carl Andren, Harris Semiconductor
BER versus Clock Offset Performance
Notes: 19
The performance of the Harris implementation is based on the performance of the symbol tracking loops. Our implementation has better tracking on the new high rate modes than the existing modes. This is due to using 1/8th chip tracking on the high rate modulation and 1/4th chip tracking on the lower rate modulations.

## Slide 20
September 8, 1997
Carl Andren, Harris Semiconductor
BER versus Carrier Offset Performance
Notes: 20
The PER curves show that the acquisition performance is still adequate out to 1.5 times the maximum offset allowed. Once you get out to 100 PPM, the performance degrades substantially. This is because the carrier phase roll becomes close to 90 degrees per symbol of the header. Exceeding 90 degrees per symbol makes the phase shift ambiguous and the modem can lock up on a sidelobe.

## Slide 21
September 8, 1997
Carl Andren, Harris Semiconductor
Processing Gain test results
Notes: 21
We ran the CW jammer test at IF over a few points to insure that the analysis was correct. The results follow the analysis reasonable well and show that the technique will pass the FCC's tests for CW jamming. We also scanned a fixed level CW signal at 12 dB PG.. over the whole band and found no problems.

## Slide 22
September 8, 1997
Carl Andren, Harris Semiconductor
Propagation Simulations